## Slide 1: About the Presentations
The presentations cover the objectives found in the opening of each chapter.
All chapter objectives are listed in the beginning of each presentation.
You may customize the presentations to fit your class needs.
Some figures from the chapters are included. A complete set of images from the book can be found on the Instructor Resources disc.

## Slide 2: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 1
First Look at Computer Parts and Tools

## Slide 3: Objectives
Learn about the various parts inside a computer case and how they connect together and are compatible
Learn how to protect yourself and the equipment against the dangers of electricity when working inside a computer case
Learn about tools you will need as a PC hardware technician and safety precautions when working around computer equipment

## Slide 4: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Laptop case – mobile
    All-in-one case – used with all-in-one computer

## Slide 5
Table 1-1 Ports used with
laptop and desktop
computers

## Slide 6
Table 1-1 Ports used with
laptop and desktop
computers

## Slide 7
Table 1-1 Ports used with laptop and desktop computers

## Slide 8
Figure 1-2 Inside the computer case

## Slide 9: What’s Inside the Case
Motherboard – sometimes called system board
  Largest and most important circuit board
Processor – central processing unit (CPU)
  Processes most of the data and instructions for the entire system
  CPUs generate heat and require a heat sink and fan (together called the processor cooler)
    A heat sink consists of metal fins that draw heat away from a component

## Slide 10: What’s Inside the Case
Expansion cards - also called adapter cards
  A circuit board that provides more ports than those provided by the motherboard
  Today, most ports are provided by motherboards
Figure 1-4 Ports provided
by a motherboard

## Slide 11: What’s Inside the Case
Memory modules – random access memory (RAM)
  Temporary storage for data and instructions as they are being processed by the CPU
  Dual inline memory module (DIMM) slots hold memory modules
Figure 1-6 A DIMM
holds RAM and is
mounted directly on
a motherboard

## Slide 12: What’s Inside the Case
Hard drives and other drives
  Hard drives may also be called hard disk drive (HDD)
    Permanent storage used to hold data and programs
  Other drives include: optical drive and tape drive
Figure 1-7 Two types of hard drives (larger magnetic drive and smaller solid-state
drive) and a DVD drive

## Slide 13: What’s Inside the Case
Power supply – also called power supply unit (PSU)
  Receives and converts house current so that components inside the case can use it
  Most come with a dual-voltage selector switch
    Allows switching input voltage from 115V to 220V

## Slide 14: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Form factors: standards that describe the size, shape, screw hole positions, and major features of computer cases, power supplies, and motherboards
  Necessary so that all will be compatible with each other
Two form factors used by most desktop and tower computer cases and power supplies:
  ATX
  Mini-ATX

## Slide 15: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
ATX (Advanced Technology Extended)
  Most commonly used form factor today
  Originally developed by Intel in 1995
  It is an open, nonproprietary industry specification
An ATX power supply has a variety of power connectors
  Power connectors have evolved because new technologies require more power
  Common ATX power connectors are listed on the following slides

## Slide 16: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
20-pin P1 connector: used by the first ATX power supplies and motherboards
4-pin and 8-pin auxiliary connectors: used to provide and additional 12 V of power for evolving CPUs
24-pin or 20+4-pin P1 connector: the older 20-pin P1 connector still worked in this connector
  Supported the new PCI Express slots
6-pin and 8-pin PCIe connectors: connect directly to the video card
  Video cards draw the most power in a system

## Slide 17: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
MicroATX form factor
  Major variation of ATX
  Reduces total cost of a system by:
    Reducing number of expansion slots on motherboard
    Reducing power supplied to the board
    Allowing for a smaller case size
  Uses a 24-pin P1 connector
    Not likely to have as many extra wires and connectors as those on the ATX power supply

## Slide 18
Figure 1-18 This MicroATX motherboard by Biostar is designed to
support an AMD processor

## Slide 19: Drives, Their Cables, and Connectors
Hard Drives
  Two standards:
    Serial ATA standard (SATA)
      Used by most drives today
    Parallel ATA (PATA) – slower than SATA
      Also called IDE interface
      Uses 40-pin ribbon cable and connector
      Two connectors on a motherboard for two data cables
      Accommodates up to four IDE devices
      Uses a 4-pin power connector called a Molex power connector

## Slide 20: Drives, Their Cables, and Connectors
Floppy drive
  3.5-inch disk holding 1.44 MB of data
  Uses a 34-pin twisted cable
  Can hold up to two drives
Figure 1-28 The notch on the side of
this floppy drive connector allows the
floppy drive cable to connect in only
one direction

## Slide 21: Protecting Yourself and Equipment Against Electrical Dangers
Important to understand electricity and how to protect yourself and equipment against it
Must learn to prevent getting shocked or damaging a component

## Slide 22: Measures and Properties of Electricity
Alternating current (AC): oscillates between negative and positive voltage
  House current is AC and oscillates 60 times in one second
Direct current (DC): travels in one direction
  Type of current used by most electronic devices
Rectifier: a device that converts AC to DC
Inverter; a device that converts DC to AC
Transformer: devices that changes the ratio of voltage to current

## Slide 23
Figure 1-30 A transformer keeps power constant but changes the
ratio of current to voltage

## Slide 24: Measures and Properties of Electricity
AC travels on a hot line from a power station
AC returns to the power station on a neutral line
When AC follows an unintended path (one with less resistance) a short can occur
  Short: a sudden increase in flow that can create a sudden increase in temperature
The neutral line is grounded to prevent uncontrolled electricity in a short
  Grounding: the line is connected directly to the earth, so that electricity can flow into the earth

## Slide 25
Figure 1-31 A polarized plug showing hot and neutral, and a three-prong plug
showing hot, neutral, and ground

## Slide 26: Protect Yourself Against Electrical Shock and Burns
When working with any electrical device, disconnect power if you notice a dangerous situation that might lead to electrical shock or fire.
Potential dangers might include:
  Power cord is frayed or damaged
  Water or other liquid is spilled near
  Device has been dropped or physically damaged
  Smell a strong electronics odor
  Power supply or fans make a whining noise
  Smoke is observed or case feels unusually warm

## Slide 27: Protect Yourself Against Electrical Shock and Burns
When working on sensitive low-voltage equipment such as a motherboard or processor:
  Ground yourself with an anti-static grounding bracelet connected to a ground
When working with power supplies, printers, and CRT monitors that contain capacitors:
  Do not ground yourself because power can flow through you to the ground and you may get shocked
  Power supplies and monitors are considered a field replaceable unit (FRU), which means you are expected to know how to replace, not how to repair it

## Slide 28: Protect Yourself Against Electrical Shock and Burns
Never use water to put out a fire (water is a conductor)
Use a fire extinguisher that is rated to put out electrical fires
Fire extinguisher ratings:
  Class A: can use water to put out fires caused by wood, paper, or other combustibles
  Class B: can put out fires caused by liquids such as gasoline, kerosene, and oil
  Class C: use nonconductive chemicals to put out a fire caused by electricity

## Slide 29
Figure 1-33 A Class C fire extinguisher is rated to put out electrical fires

## Slide 30: Protect the Equipment Against Static Electricity or ESD
Electrostatic discharge (ESD): electrical charge at rest
  When two objects with dissimilar electrical charges touch, electricity passes between them until charges are equal
ESD can cause two types of damage:
  Catastrophic failure: destroys the component
  Upset failure: damages the component so that it does not work well
  Both types permanently affect the device

## Slide 31: Protect the Equipment Against Static Electricity or ESD
To protect against EDS, always ground yourself with one or more of the following static control methods:
  Ground bracelet: also called ESD strap, antistatic wrist strap, or ESD bracelet
    Attach bracelet to the computer case to ground it
  Ground mats: also called ESD mats
    Often used by bench technicians who repair and assemble computers at workbenches or assembly lines
  Static shielding bags: also called antistatic bags
  Antistatic gloves: also called ESD gloves
    Prevents ESD between you and a device when wearing

## Slide 32: Protect the Equipment Against Static Electricity or ESD
Rule 1: When passing a circuit board or other component to another person, ground yourself and touch the other person before you pass it
Rule 2: Leave components inside antistatic bags until ready to use them
Rule 3: Work on hard floors, not carpet
Rule 4: Don’t work on a computer in a cold and dry atmosphere
Rule 5: Remove packing tape and cellophane from around work area (materials that attract ESD)
Rule 6: Keep components away from hair and clothing

## Slide 33: Tools Used By a PC Repair Technician
Essential tools
  Ground bracelet, ground mat, antistatic gloves
  Flat-head screwdriver
  Phillips-head or cross-head screwdriver
  Torx screwdriver set (size T15)
  Insulated tweezers
  Extractor
  OS recovery CD or DVD
Many other non-essential tools exists
Use a toolbox

## Slide 34
Figure 1-38 Tools used by PC support technicians when maintaining,
repairing, or upgrading computers

## Slide 35: Post Diagnostic Cards
Post Diagnostic Cards
  Helps discover, report computer errors and conflicts at power-on self test (POST)
    Tests performed by startup BIOS
Figure 1-41 Post Code Master
Diagnostic card by Microsystems
Developments, Inc. installs in a
PCI slot

## Slide 36: Post Diagnostic Cards
BIOS (basic input/output system)
  Data and instructions stored on ROM chips
  ROM BIOS chips: type of firmware
Three purposes served by motherboard ROM BIOS
  System BIOS: manages simple devices
  Startup BIOS: starts the computer
  BIOS setup: changes motherboard settings
CMOS RAM: includes date, time, port configurations
Flash ROM
  ROM chips that can be overwritten

## Slide 37: Power Supply Tester
Power Supply Tester
  Measures output of each power supply connector
Figure 1-42 Use a power supply tester to test the output of each power
connector on a power supply

## Slide 38: Multimeter
Multimeter
  Measures several characteristics of electricity in a variety of devices
Figure 1-43 This digital multimeter
can be set to measure voltage,
resistance, or continuity

## Slide 39: Loopback Plugs
Loopback plug
  Used to test a port in a computer or other device to make sure the port is working
    May also test the throughput or speed of port
Figure 1-44 A loopback plug testing
a network port and network cable

## Slide 40: Proper Use of Cleaning Pads and Solutions
Most cleaning solutions contain flammable and poisonous materials
  Take care when using them
  A Material Safety Data Sheet (MSDS) explains how to properly handle substances such as chemical solvents and how to dispose of them
    Usually comes packaged with chemical
  Organizations may require an accident report be filled out if accident occurs using dangerous products

## Slide 41
Figure 1-45 Cleaning solutions and pads

## Slide 42: Managing Cables
Make sure cables are in a safe place
  People can trip over cables left on floor (called a trip hazard)
If cable must be ran across a path or where someone sits:
  Use a cable or cord cover

## Slide 43: Lifting Heavy Objects
Follow these guidelines to avoid back injury:
  Decide which side of object to face so that the load is most balanced
  Stand close to the object with feet apart
  Keep back straight, bend knees and grip load
  Lift with legs, arms, and shoulders (not with back or stomach)
  Keep the load close to your body and avoid twisting your body while holding it
  To put object down, keep back straight and lower object by bending knees

## Slide 44: Summary
Ports on a computer might include video, network, sound, S/PDIF, USB, FireWire, eSATA, and PS/2
Internal computer components include the motherboard, processor, expansion cards, DIMM modules, hard drive, optical drive, floppy drive, tape drive, and power supply
Form factors used by cases, power supplies, and motherboards are ATX and MicroATX
Power connectors include the 20-pin P1, 24-pin P1, 4-pin and 8-pin auxiliary motherboard, 4-pin Molex, 15-pin SATA, 4-pin FDD, 6-pin PCIe, and 8-pin PCIe

## Slide 45: Summary
Standards used by hard drives and other drives to interface with motherboard and power supply are serial ATA (SATA) and parallel ATA (PATA)
Units used to measure electricity include volts, amps, ohms, joules, and watts
Microcomputers require DC which is converted from AC by the PC’s power supply
A power supply and CRT monitor contain dangerous charges even when unplugged
Never use water to put out an electrical fire

## Slide 46: Summary
To protect against ESD use a ground bracelet, ground mat, antistatic bags, and antistatic gloves
Special tools a PC support technician might need include a POST diagnostic card, power supply tester, multimeter, and loopback plugs
A MSDS explains how to handle chemicals
Be careful not to lift a heavy object in a way that can hurt your back
Make sure cables are not trip hazards