## Slide 1
AIR RIFLE SAFETY & RANGE PROCEDURES
JROTC Marksmanship Training, Section V

## Slide 2
Air Rifle Safety & Range Procedures
Section Objective: To learn about gun and range safety and the actions that JROTC cadets must perform to safely participate in air rifle marksmanship

## Slide 3: Air Rifle Safety Training
Safe Gun Handling Rules
Shooting Range Basics
Range Commands
Protecting Your Health
Everyone is a Safety Officer
Range Firing Procedures
Self-Discipline & Focus
Becoming “Marksmanship Qualified”

## Slide 4: Safety Performance Objectives
Properly Trained Cadets Will:
Be aware of the gun muzzle and maintain proper muzzle control at all times
Check for and maintain an open action, with CBI properly inserted, on every gun they handle
Keep fingers off of the trigger at all times until actually aiming at a target
Respond properly to range commands and special range situations
Be aware of the gun handling of those around them to assist others in following safe gun handling rules

## Slide 5: Learning To Handle Guns Safely
The goal—eliminate all gun accidents!
Know primary gun parts that affect safety: M-A-T
Apply M-A-T performance standards
Practice handling air rifles--safety comes from practice, not knowledge
Safe gun handling rules apply to all guns and firearms

## Slide 6: Primary Gun Parts that Affect Safety
3. Trigger 2. Action 1. Muzzle

## Slide 7: How Air Rifle Actions Function
Air rifle actions have a bolt or action that can be opened or closed. Opening the action exposes the breech (rear) end of the barrel for loading. Opening and closing the bolt/action cocks the firing mechanism to prepare the rifle for firing.
Daisy M853-bolt in open position, pulled to rear
Close bolt by pushing forward
Pressing the trigger to the rear releases the mechanism to fire the loaded rifle

## Slide 8: CBI—Clear Barrel Indicator
CBI (Clear Barrel Indicator) confirms that rifle is unloaded
CBI must be in rifle at all times except during preparation and firing
CBI removed on firing line when preparation for firing begins
When firing is complete, ground rifle, insert CBI
Keep CBIs clean and off the floor Inserting CBI
Inserting CBI

## Slide 9: Rule 1--Muzzle Control
1st gun handling rule: control the direction the muzzle points
Point the gun in a safe direction—usually upward or downrange towards the targets
Never point a gun at another person
Carry guns with the muzzle above head level

## Slide 10: Rule 2—Action Open
OPEN AIR RIFLE ACTIONS
2nd gun handling rule--keep gun action open, except when firing
Visually check the action to verify that it is open
Keep a CBI inserted to confirm that the action is open
A gun with an open action cannot be fired unintentionally
On target ranges, actions must remain open at all times, with CBIs inserted, except when the rifle is on the firing line and dry or live firing is authorized

## Slide 11: Rule 3—Finger Off Trigger
3rd gun handling rule--keep fingers outside of trigger guard except when aiming
The trigger guard protects the trigger from being unintentionally pulled
Place the index finger on the trigger only after starting to aim at the target

## Slide 12: Safety Rules Apply to All Guns
Open Action
Open Action with Safety Flag
Muzzle Control
Safe Gun Handling Rules Apply to all guns in all circumstances

## Slide 13: Air Rifle Range Layout
Range Officer Area
Range Officer Station
Ready Line
Ready Area
Firing Distance = 10 meters
Firing Line
Firing Points
Targets & Backstops
Safety Barrier

## Slide 14: Range Rules
Range Officer: In charge of range, RO must be an adult, adult RO must be present
Firing Point: One for each shooter
Target Holder/Backstop: One for each firing point
Firing Line: No part of the body may touch the firing line or the floor ahead of line
Ready Line: Persons waiting to fire & spectators must remain behind line

## Slide 15: Range Safety Conditions
Line is “Hot”:
No one is forward of firing line
Line is ready for firing
Call to Firing Line:
OK to move rifle and equipment to firing line
Handling rifles may be permitted, CBIs remain in
Preparation Period:
OK to remove CBIs, close bolts and dry-fire or do aiming exercises
Charging gas or loading is not authorized
Unloaded Rifle:
Action open
No pellet in barrel
CBI inserted
Grounded Rifle:
On floor or bench
Unloaded w/CBI inserted
Line is Clear:
Rifles are unloaded, grounded and checked
No one handles rifles

## Slide 16: Basic Range Commands
LOAD
OK to charge gas mechanism
OK to insert pellet
OK to close action
Not OK to shoot
START
OK to begin firing
OK to continue firing
When last shot is fired—open action, insert CBI, ground rifle
STOP
Immediately stop attempting to fire shot (finger off trigger!)
Firing no longer authorized
UNLOAD
Open action and ground rifle
Notify RO if rifle remains loaded
RO must confirm unloaded condition--RO assistance is required to unload loaded rifles

## Slide 17: Safe Loading Procedure
1.Open Action
2.Charge Air
3.Insert Pellet
4.Close Action
5.Place rifle in position and fire shot
6.Open action--repeat
Open action, charge air lever, then insert pellet
Insert pellet here, then close bolt

## Slide 18: Dry Firing
Dry Firing: Cocking and releasing trigger mechanism, without charging gas system, to simulate firing
Will not damage air rifles
Some air rifles cannot be dry fired (Daisy M887/888); aiming exercises can be done in lieu of dry firing
An especially effective way to practice
Where: Only on designated firing point
When: When authorized by RO (e.g. practice or preparation periods)
Do not charge air during dry firing--just open and close action to cock trigger mechanism

## Slide 19: Range Safety Procedures
Malfunctions
Stay in position
Keep rifle pointed downrange
Raise Hand
Wait for RO to inspect rifle and give instructions

## Slide 20: Range Safety Procedures
Firing Completed
Immediately open action
Get out of firing position
Ground rifle
Insert CBI
Wait for instructions

## Slide 21: Range Safety Procedures
Discharging loaded rifle into PDC
Loaded Rifle after STOP-UNLOAD
Remain in position
Keep rifle pointed downrange
Raise Hand
Wait for RO to give instructions to fire rifle in PDC (Pellet Discharge Container) or backstop

## Slide 22: Personal Safety & Hygiene
Pellet Handling Hygiene
Lead is toxic
No food on range
No open beverage containers
WASH HANDS AFTER HANDLING PELLETS
Safety Glasses
Wearing safety or eyeglasses during air rifle firing is recommended (required in NJROTC)
Personal Clothing
Sweatshirt or work shirt
Glove (for hand that holds or supports rifle)
Note: Hearing protection is not required for air rifle

## Slide 23: Gun Cases
Gun Cases:
Used to store and transport air rifles
Behind firing line—keep rifles in closed cases
Bring closed case to firing line with muzzle oriented downrange
After opening case—open action and insert CBI
Remove rifle from case, ground rifle, remove case from firing line
After firing—replace rifle in case on firing line—CBI may be removed, action closed and trigger released before closing case

## Slide 24: Special Conditions
Safeties
Mechanical devices to facilitate carrying loaded guns
On target ranges, the safety is the open action and CBI
Most target air rifles do not have mechanical safeties
The use of the mechanical safety is not required in air rifle target shooting
Safe Air Rifles for Target Ranges
Use only 4.5mm/.177 cal. air rifles
Use only air rifles with pellet velocities of 600 fps or less
Taking a Break
Never lay a loaded rifle down
Rifle must be cleared with a CBI inserted before laying it down
Some ranges may have special safety rules—they must be followed too

## Slide 25: Achieving a Perfect Safety Record
Safety requires self-discipline and focus--you are the most important component of safety
Everyone is a Safety Officer
Never tolerate unsafe gun handling by others
Act immediately to correct unsafe situations
Anyone can call STOP in a safety emergency
Remember the Goal—Eliminate All Gun Accidents!

## Slide 26: Becoming Marksmanship Qualified
Cadets must attend safety training class
Cadets must pass a standardized safety exam
Exam based on safety training class and Cadets Guide to Air Rifle Safety
Cadets must sign Cadet Safety Pledge
Enjoy your rifle marksmanship experience!